## Slide 1
Introduction to QoE and Its Relationship with Usability
Mikołaj Leszczuk, Zdzisław Papir, Lucjan Janowski, Jakub Nawała
Notes: This is what we are doing on a daily basis.
We say multimedia here, but we mainly work with videos (usually w/o sound). Such a limitation of context necessary because we are dealing with a difficult problem.

## Slide 2: Presentation Outline
Multimedia Quality of Experience (QoE)
Subjective Methods of Measuring QoE
Objective Methods for Measuring QoE
Quality of Experience and Its Relationship with Usability

## Slide 3: Multimedia Quality of Experience (QoE)

## Slide 4
(graphics: Media Trendy 2008)
Caring about the perceived quality of multimedia services (Quality of Experience) is essential for service and content providers:
  due to competition between providers
  in the face of changing ways to use the media.
Notes: It is the end-user’s satisfaction that makes your service better than others. The problem is - the demand for quality is constantly rising.

## Slide 5: Internet TV, Video on Demand...
Daniel Minoli - „Video Dialtone Technology” 1995
There is now feverish activity in telecommunications, CATV, ISPs to deploy the Information Superhighway...
A key driver of the Information Superhighway is video.
Thomas Miki - ComMag 1994
The battle has begun, and only those carriers who provide the highest level of performance, reliability, and flexibility
will be the winners.
Notes: Wspomnienie – okres PTK Kraków, projekty BBL oraz BTI (Polska-Dania), Lucent

## Slide 6
Larger Volume & Demand
According to Cisco [1]
  3-fold increase in IP traffic over the 5 years (from 2017)
  82% of all IP traffic is IP video traffic (in 2022)
  7-fold increase in video surveillance traffic (2017 - 2022)
[1] Cisco Visual Networking Index: Forecast and Methodology, 2017–2022. White Paper. Cisco Systems, Inc., 26 Nov. 2018
Notes: It is nice to reference such forecasts in an introduction section of your thesis (if it is related with multimedia).
Larger volume & larger demand begs for better quality (and also is a result of better quality being used).
This is a 4 fold growth in the plot on the right.
EB = exabytes = 1 million TB
There are much more forecasts so do not hesitate to take a look on your own.

## Slide 7: Technology Enablers...
BANDWIDTH
AVAILABILITY OF BANDWIDTH – wireless
home
travel
office
SCALABLE VIDEO CODING – stream bit-rate
adaptation to the network
(D)WDM
GbE
HFC
FTTx, xDSL
PLC, UWB Wi-Fi
CACHING – Content Delivery Networks (CDNs)
HDTV
SDTV
PC
Mobile TV
Notes: We went a long road to reach a point in which we are today.
I (i.e., JN) don’t know about you, but I prefer to consume content through a wireless network. In fact, I do not have a fixed internet connection in my home.
CDNs are a large part of what makes Netflix look good in comparison to competitors.

## Slide 8: Technology Enabler – Upload Bandwidth
Media Personalization
Injecting Advertisements
Citizens' Journalism
Internet Encyclopaedias
Photo Services
New ways to use the media
Notes: We are not only the consumers, but also the producers.

## Slide 9
Upload Increase
According to Cisco [1]
  the average internet user generated 84.6 GB of traffic per month (by 2022)
  up 194% from 28.8 GB in 2017
[1] Cisco Visual Networking Index: Forecast and Methodology, 2017–2022. White Paper. Cisco Systems, Inc., 26 Nov. 2018

## Slide 10: Quality of Service
bandwidth
delay
losses
VOICE TRANSMISSION
VIDEO TRANSMISSION
DATA TRANSMISSION
Notes: Mówimy o opóźnieniu, przepustowości oraz stratach ruchu. Tu pokazujemy wymagania per-serwis.
QoS - possible to be objectively measured. I can measure a time, delay and number of lost packets.
Various transmissions are sensitive to various degrading factors:
Voice transmission - requires low bandwidth, but sensitive for the delay
Data transmission - may require high bandwidth, but can tolerate the delay
Video transmission - requires high bandwidth, is able to recover from losses, but does not tolerate the delays

## Slide 11: Quality of Experience (QoE)
Quality of Service (QoS), not enough for service providers
Real challenge - Quality of Experience (QoE)
Global issue, significant trend in development of multimedia systems
For video: Video Quality Experts Group
Notes: I know how many packets I have lost, but what does the end-user think about it? - the question many board members of Internet Provider companies asked

## Slide 12: QoE by White Book of QUALINET Network
The QoE research topic is related to the “degree of contentment or annoyance of the user of the application or service. QoE results from the fulfillment of the user's expectations regarding the usability and/or satisfaction of the application or service in the light of current user preferences.”
Notes: There is a newer definition from The QoE Book
QoS - objective
QoE - subjective
Current preferences and expectations are important phrases here.

## Slide 13: QoE by The QoE Book
“Quality of Experience (QoE) is the degree of delight or annoyance of a person whose experiencing involves an application, service, or system. It results from the person’s evaluation of the fulfillment of his or her expectations and needs with respect to the utility and/or enjoyment in the light of the person’s context, personality and current state.”
Adapted from Möller, S., & Raake, A. (Eds.). (2014). Quality of Experience. https://doi.org/10.1007/978-3-319-02681-7

## Slide 14: Aspects of Media Ecosystem
Content
Delivery
Usability and Interaction
Business Model
QoE
Notes: QoE as a point of contact between all of those.
QoE has a significant impact

## Slide 15: Quality of Service? Quality of Experience?
Notes: Vertical axis denotes a layer. At the top - (there should be) a user of the client & owner of the server.
QoS - countable and easier to measure.
QoE - difficult to measure, but better correlates to actual quality.

## Slide 16: Quality of Experience
Notes: QoE includes QoS

## Slide 17: Multimedia Quality Problem
Over-The-Top (OTT) video streaming
Multimedia market competition
Quality-driven customer churn
What is far end quality?
By VIA Gallery from Hsintien, Taiwan – VIA QuadCore @ Computex 2011-Smart TV Video on Demand, CC BY 2.0, https://commons.wikimedia.org/w/index.php?curid=38934022
Notes: The demand for quality is constantly rising. Whenever I can compare some old solution with the new one, the old is rated lower than before.

## Slide 18: Subjective Methods of Measuring QoE

## Slide 19
Quality of Experience (QoE)
The degree of delight or annoyance of a person
The person experiences an application, service, or system
The QoE results from the fulfillment of the person’s expectations and needs wrt utility and/or enjoyment
All that in the light of person’s context, personality and current state
Adapted from Möller, S., & Raake, A. (Eds.). (2014). Quality of Experience. https://doi.org/10.1007/978-3-319-02681-7
Notes: wrt = with respect to
User-centric approach
Relative to the current user’s expectations
Strongly connected with the way we perceive the world

## Slide 20: From Quality of Service (QoS) to Quality of Experience (QoE)
What we build
What we want
Quality model
QoS
Pixels
Calibration
QoE
What we know
Notes: The next slide: so how do you get the calibration data?

## Slide 21
Idea
Subjective scores (i.e. calibration data) = ground truth
Vary contents to measure the quality
  Everything else should stay the same
Use the scores to improve your predictions about the quality (i.e., build a better-quality model)
Notes: Subjective scores - so called ground truth (i.e., provided by direct observation and not coming from inference)
Controlled environment - get rid of, hopefully, all confounding factors.

## Slide 22: Obtaining Calibration Data
Perform a “subjective test”
Subjective scores as a result
Basically, subjective scores
Hundreds to thousands needed
Various content, quality, people, etc.
Homogeneous conditions
Notes: Subjective Methods for Measuring QoE start here - must be done on 29/30 Nov

## Slide 23: Building of AGH Institute of Telecommunications

## Slide 24: QoE Laboratory - Outside

## Slide 25: QoE Laboratory - Inside

## Slide 26: Laboratory of multimedia tests

## Slide 27: Idea of Psychophysical Experiments (Subjective Tests)
User opinion = final score
Asking users about quality while using service - difficult or impossible
Subjective experiment - often best option to collect users' opinions
Controlling distortions
Controlling use case
Notes: User opinion - so called ground truth (i.e. provide by direct observation and not coming from inference)
Controlled environment - get rid of, hopefully, all confounding factors.

## Slide 28: Practical Realisation of Subjective Experiment

## Slide 29: Naming Conventions of Psychophysical Experiments (Subjective Tests)
Sources (SRC)
Hypothetical Reference Circuits (HRC)
Processed Video Sequences (PVS)
Mean Opinion Scores (MOS)
Notes: Explain the terms

## Slide 30
Content is Important
Different expectations from different contents
Examples:
  Sport,
  News,
  Cartoon.
Try to accomodate for the whole scale of qualities
Images taken from the VQEG’s Report on the Validation of Video Quality Metrics for High Definition Video Content

## Slide 31
Testers are Important
Different expectations depending on a social group
Examples:
  age groups,
  ethnic groups,
  level of advancement groups
Notes: The level of advancement - one can be a naive user or an expert.

## Slide 32
Environment is Important
Lighting conditions
Display size
Distance from the display
Is tester sitting on a chair or a sofa?
Is there anything that can distract the tester?
Notes: Those are one of the most important factors defining whether your test can be compared with any other test.
We have a sofa in our QoE laboratory (the B9 building, 1st floor). It is good for having internal meetings as well as for testing!

## Slide 33
Training is Important
We want to have the data of good quality
The tester must know how to use a testing interface
Notes: quality data - garbage in, garbage out if the tester does not know what one is doing

## Slide 34
We want repeatable results (that can be compared among many laboratories)
Why do We Care?

## Slide 35: Absolute Category Rating
Training & actual experiment sessions
Each sequence rated individually (ACR scale)
Labels on scale: bad, poor, fair, good, excellent
Translated to values 1-5 when calculating MOS
Notes: PVSs rated one-by-one; no explicit comparisons; labelled, ordinal scale

## Slide 36: Analysis of Results – Average
By Cmglee – Own work, CC BY-SA 3.0, https://commons.wikimedia.org/w/index.php?curid=15147460
Average (mean) score for each:
  Subject
  PVS
  HRC
Mode and median less common
Notes: Notice how the mean differs for distributions having the same median.

## Slide 37: Analysis of Results – Normal Distribution
Each subject – different rating patterns
Some subjects not using entire scale
But histogram to look normally distributed

## Slide 38: Analysis of Results – Student’s t-Test
t-Test – statistical hypothesis test
Used to determine if two sets of data significantly different from each other
Most applied when normal distribution
Testing e.g., if perception threshold quality distinguishable from SRC quality

## Slide 39: Analysis of Results – Modelling using Sigmoid (Logistic) Function
By Qef (talk) – Created from scratch with gnuplot, Public Domain, https://commons.wikimedia.org/w/index.php?curid=4310325
Notes: It is most often used to weigh the importance of some phenomena (e.g. brightness or contrast).

## Slide 40: Analysis of Results – Outliers
By Osrecki – Own work, CC BY-SA 4.0, https://commons.wikimedia.org/w/index.php?curid=48650484

## Slide 41: Dark Side
Subjects scoring whole experiment not just single sequence
Correct experiment needing careful preparation
In general asking people about anything – tricky
Obtained conclusions to consider experiment limitations
Notes: Problem of comparing results from different experiments

## Slide 42: Objective Methods for Measuring QoE

## Slide 43
What we build
What we want
Quality model
QoS
Pixels
Calibration
QoE
What we know
From QoS to QoE
Notes: Slide from the previous presentation
Quality model - this is the objective method measuring the QoE

## Slide 44
What are Those?
Algorithms using objectively measurable input and providing objectively measurable output
For example: “give me a video and I will tell you what an average end-user thinks about its quality”
You want to replace a human with an algorithm

## Slide 45
Why Objective Methods?
Objective - “based on real facts and not influenced by personal beliefs or feelings” (from Cambridge Dictionary)
Cheaper
  CPUs are much faster than humans (if it comes to digital images processing)
Scalable
  Assessing the quality of multiple sources
Notes: It is safer to build a business based on something objective.
Cheaper - assessing the quality in non-objective way means contacting your end-users (how many do you have?)
Scalable - currently, in TV head-ends, there are people just sitting and watching everything that goes on-air

## Slide 46: Classification
Full access to the original content
Computationally intensive
Good for content producers (and modifiers)
No access to the original content
Faster than FR methods
Scalable
Full Reference
No Reference
Notes: No Reference (NR):
-> scalable: NR probe can be attached at any point there is access to a video signal
There are also Reduced Reference (RR) and mixed methods, but they are not so popular.

## Slide 47: PSNR
Examples
Full Reference
The most popular
Based on Mean Squared Error (MSE) metric
Used in Shot Boundary Detection (SBD)
For details, see here
Notes: I gave here equations without deep explanation. For details please refer to the laboratory instruction.

## Slide 48: VMAF
Examples
Full Reference
Perceptual video quality assessment based on multi-method fusion
State-of-the-art
Created by Netflix, Inc.
Click the Octocat to go to its repository
Notes: I didn’t use Netflix’s logo, because it is not legal to do so without their prior consent. The story is different if it comes to Octocat that links to GitHub.

## Slide 49: Implementation of Key Performance Indicators (KPIs) for Quality Measurement
No Reference
Notes: Objective measurement of QoE starts here - present it on Dec, 6 2018
Not only implementation, but also the general description
Special type of quality - subjectively perceived quality

## Slide 50: General Information
Algorithmic approach to visual quality assessment:
repeatable
easy to manipulate
countable
implementable
Notes: Repeatable: more stable than asking people about the quality
Easy to manipulate: possible to map it to other measures, one may look for correlation between various phenomena, in general, application of mathematics is possible!
Countable: good medium for comparison of various visual materials
Implementable: can be (and was) transferred to both software and hardware solutions

## Slide 51: General Information
Measurement targeting many artifact sources:
capturing
processing
transmission
display
Notes: capturing: optics non-ideality
processing: mainly compression and rescaling
transmission: lossy medium
display: low dynamic range, smaller colour gamut
targeting specific distortions should give higher accuracy

## Slide 52: General Information
Results reflecting subjectively perceived quality:
correlation with human perception of visual artifacts
signal-based approach (so called No-Reference approach)
Notes: KPIs - objective quality measure (any numerical value),
People’s opinion - subjective quality measure (usually Mean Opinion Score)
Non-trivial goal - in practice, one has to run subjective tests
If human perception is the most important, then let’s focus on visual signal and not compression, transmission parameters and so on

## Slide 53: No-Reference Approach
Opposite to Full-Reference approach
Easily applicable to many scenarios:
  No-Reference probe can be attached at any point of content delivery chain
  no need of source material
  access to visual content as the only one requirement
Notes: Full-Reference is a classical approach - take each pixel from unmodified image and compare it with associated pixel in modified image
source material - unmodified, original, high-quality visual content (no compression, no lossy transmission)
One does not need to have knowledge about transmission, compression and display parameters

## Slide 54: No-Reference Approach
Non-trivial:
based on Human Visual System (HVS) response to visual artifacts
no information about compression and transmission parameters
no direct way to compare with source material
Notes: Not everyone has the same sensitivity for visual artifacts
It is not possible to apply simple pixel-to-pixel algorithm comparing modified and unmodified visual material

## Slide 55: Other Approaches
Full-Reference:
applicable when source material is accessible
usually computationally intensive
good for content producers/modifiers
Notes: In practice, this approach achieves higher correlation with subjectively perceived quality
Standardised approach used by many important players (e.g., Netflix)
Classical, well-defined

## Slide 56: Other Approaches
Reduced-Reference
  only some parameters about the source material and its processing are available
Bitstream-based
  no need to access visual signal
  ongoing development by standardisation parties
Notes: Bitstream-based:
  one wants to say as much as possible about the visual content by looking on the transport layer (but not only)
  can be applied at many points of delivery chain
  can be used with encrypted signal
  modular build: if only transport level - transport level measurements, if more - more

## Slide 57: Our Implementation
15 Video Quality Indicators (VQIs)
Implemented in C
Binary executables freely available online at: http://qoe.agh.edu.pl
Source code available for research upon request
Notes: VQIs is just our name for KPIs
C implementation makes it easy to port the algorithms to various platforms
Tested quite well (e.g., by licensing parties)

## Slide 58: Example: Blur VQI
Notes: Execution flow:
  Read Y channel from YUV image,
  Find edges using Sobel filter,
  Measure width of edges
    Only a subset of existing edges are chosen (based on dynamically calculated threshold value derived from standard deviation for a given macro block)
  Result is proportional to mean width of edges

## Slide 59: Quality of Experience and Its Relationship with Usability

## Slide 60: Definitions
Usability (ISO 9241-11): effectiveness, efficiency, satisfaction in a context of use
QoE: delight/annoyance from service/application/system
Common element: user satisfaction

## Slide 61: Key Differences
QoE → focuses on media/service quality
Usability → focuses on interaction design
QoE is content- and network-driven; Usability is task- and interface-driven

## Slide 62: Intersections
Both influence overall User Experience (UX)
Example: A video streaming app may have excellent QoE (smooth playback) but poor usability (confusing navigation) → dissatisfaction

## Slide 63: Takeaway
QoE and usability are complementary
Joint evaluation is crucial for holistic understanding of UX